## Slide 1
DAB Stack
ODR-mmbTools · Containerised Digital Audio Broadcasting
Architecture · Signal Flow · SNMP Monitoring · OpenNMS Integration
Mode A
Software / Dev
Mode B
USRP B200 RF
Docker
4 containers
OpenNMS
SNMP v2c

## Slide 2
Full Stack Architecture
How the four containers talk to each other
Radio Caroline
:10001
Flash On Air
:10002
XRadio
:10003
dab_encoder
ODR-AudioEnc
VLC → DAB+ EDI
EDI tcp
:10001-3
dab_mux
ODR-DabMux
Ensemble: Solent Uni
EDI tcp
:13000
dab_mod
ODR-DabMod
Mode A: /dev/null
RF Out
/ /dev/null
dab_net (internal Docker bridge)
dab_collector
Ubuntu 24 + snmpd
pass_persist.py
ZMQ
Telnet
Telnet
:2120
SNMP
UDP :161
OpenNMS
NMS / Monitoring
Host machine :8980

## Slide 3
DAB Signal Flow
From internet radio stream to DAB ensemble output
1
Internet Stream (VLC pull)
ODR-AudioEnc uses VLC to pull live HTTP/Icecast streams for each subchannel. Three parallel encoder instances handle Radio Caroline, Flash On Air and XRadio.
bitrate 64 kbps · DAB+ · protection 3
2
DAB+ Encode → EDI
Each stream is AAC-LC encoded at 64 kbps, wrapped in EDI (Ensemble Data Interface) and pushed to the Mux on dedicated TCP ports 10001–10003.
EDI tcp push · port per subchannel
3
Multiplex (ODR-DabMux)
DabMux assembles the ensemble: combines three subchannels, injects FIG headers, applies TIST timestamps and outputs an EDI stream on port 13000 for the modulator.
Ensemble: Solent Uni · Mode 1 · ECC 0xe1
4
Modulate (ODR-DabMod)
DabMod reads the EDI feed, applies root-raised-cosine filtering and OFDM modulation. Mode A outputs IQ samples to /dev/null; Mode B drives the USRP B200 at 229.072 MHz.
DAB Mode 1 · 2.048 Msps · digital gain 0.8

## Slide 4
Collector — SNMP Bridge to OpenNMS
How pass_persist.py bridges ZMQ/Telnet stats into SNMP OID space
dab_mux
ZMQ port 12720
Buffer stats / sub states
dab_mod
Telnet :2120
Restarts · EDI · gain · rate
pass_persist.py
dab_collector
1. Poll ZMQ & Telnet
2. Cache metric values
3. Serve OID GET/GETNEXT
4. snmpd pass_persist proto
snmpd
UDP :161
v2c community: public
OpenNMS
:8980
Custom OID Tree .1.3.6.1.4.1.8072.1.3.2.99
.99.1.1.x
Sub 1: Radio Caroline
Buffer max/min
Underruns / Overruns
Peak L/R dBfs
State · Uptime
.99.1.2.x
Sub 2: Flash On Air
Buffer max/min
Underruns / Overruns
Peak L/R dBfs
State · Uptime
.99.1.3.x
Sub 3: XRadio
Buffer max/min
Underruns / Overruns
Peak L/R dBfs
State · Uptime
.99.2–3.x
Mux Output + Mod
Output connections
Mod restarts
EDI timestamp
Gain · Sample rate

## Slide 5
Operating Modes
Mode A — development & testing · Mode B — live RF broadcast
MODE A
Software Only
Purpose
Development / testing — no hardware
Modulator output
/dev/null (IQ samples discarded)
Frequency
N/A
Ensemble label
Solent Uni
USB passthrough
Not required
Build time
~5 min (no UHD firmware)
Start command
docker compose -f ... mode_a up -d
MODE B
USRP B200 Live RF
Purpose
Live DAB broadcast over the air
Modulator output
USRP B200 SDR (libuhd)
Frequency
229.072 MHz — DAB Channel 12D
Ensemble label
Solent Demo
USB passthrough
Required (/dev/bus/usb)
Build time
~15–20 min (UHD firmware download)
Start command
docker compose -f ... mode_b up -d
⚡ Only run one mode at a time — always stop the stack before switching

## Slide 6
Ports, Health & Debug
Port
Proto
Purpose
Exposed to
10001–3
TCP
EDI audio → mux
dab_net
12720
TCP
Mux ZMQ mgmt
127.0.0.1
12721
TCP
Mux Telnet ctrl
127.0.0.1
13000
TCP
EDI mux → mod
dab_net
2120
TCP
Mod Telnet ctrl
127.0.0.1
9400
TCP
Mod ZMQ ctrl
127.0.0.1
161
UDP
SNMP (collector)
dab_net
Quick Debug
Live stats snapshot
docker exec -it dab_collector
python3 /collector/debug.py
Live loop (5 s)
docker exec -it dab_collector
python3 /collector/debug.py --loop 5
SNMP walk (DAB tree)
snmpwalk -v2c -c public <IP>
.1.3.6.1.4.1.8072.1.3.2.99
Subchannel 1 state
snmpget -v2c -c public <IP>
.1.3.6.1.4.1.8072.1.3.2.99.1.1.7
Follow mux logs
docker logs -f dab_mux
Healthy Values
Subchannel state:
running
Buffer fill:
> prebuffering threshold
Underruns / Overruns:
0
Mod restarts:
0